## Slide 1: Organic Transistors
By Prasann Viswanathan
190070047

## Slide 2: Outline
Device physics and parameters
Materials used in fabrication
Fabrication techniques
Current applications in industry
Future plans of work

## Slide 3: Device Physics and Parameters
J. Chang, Z. Lin, C. Zhang, and Y. Hao, "Organic Field-Effect Transistor: Device Physics, Materials, and Process", in Different Types of Field-Effect Transistors - Theory and Applications. London, United Kingdom: IntechOpen, 2017
Carrier Mobility
  Temperature and Field dependent
I-V characteristics in different modes of operation
  Linear
  Saturation
On current to Off current ratio
Threshold voltage

## Slide 4: Materials
Substrate
  Quartz, glass, silicon wafer. Polycarbonate, polyimide
Electrodes
  Metals: Gold, palladium, magnesium, aluminium. Non-metal: graphite, 10-CSA doped polyaniline
Dielectric Layer
  Ta2O5, Barium zirconate titanate (BZT)
Semiconducting Layer
Image from: Materialscientist, CC BY-SA 3.0 <https://creativecommons.org/licenses/by-sa/3.0>, via Wikimedia Commons

## Slide 5: Semiconducting Layer
Different charge transport nature
P-type
  Polycyclic aromatic compounds
  Pentacene, rubrene
N-type
  Scarcer than P-type
  Lower performance and unstable in ambient conditions
  Perfluoropentacene, Naphthalene-diimide with cyanides
Chandar Shekar, B., Lee, J. & Rhee, SW. Organic thin film transistors: Materials, processes and devices. Korean J. Chem. Eng. 21, 267–285 (2004).

## Slide 6: Fabrication Techniques
Vacuum Evaporation
  Extremely low pressures
  Expensive and only for small molecules
Solution Deposition
  Cost effective method
  Material must be soluble or dispersible in medium

## Slide 7: Continued
Thin Film Alignment
  Alignment provides better mobility
  Mechanical/ Growing crystals/ Field-induced/ Solution-processed/ Direct deposition
Patterning
  Eliminating parasitic leakage and cross talk
  Different methods

## Slide 8: Applications in Industry
Flexible displays and e-papers
  iPhone covers with flexible displays
  Philips with E-Ink demonstrated 85 dpi active-matrix backplane with bend radius 2cm
Biosensors
  Mainly voltage transducers
  Glucose level detection, X-Ray imagery and fingerprint sensing
Simple logic circuit applications
  RFID cards, smart cards and disposable sensors
Image by: X. Guo et al., ”Current Status and Opportunities of Organic Thin-Film Transistor Technologies,” in IEEE Transactions on Electron Devices, vol. 64, no. 5, pp. 1906-1921, May 2017.

## Slide 9: Conclusion and Future Improvements
Lack of material stacks to produce high performance, stable and uniform Organic Transistors
Lack of standardisation of material, device integration and manufacturing methods
Trade-offs between large scale, low-cost processing and performance
Defining focused applications

## Slide 10: Thank you!